## Slide 1: Network Switching
Course Code: COE 3201
Dept. of Computer Engineering
Faculty of Engineering
Lecture No: | 12 | Week No: | 13 | Semester: | 
Lecturer: |  |  |  |  | 
Course Title: Data Communication

## Slide 2: Lecture Outline
Switching Mechanism for Data Transfer
Circuit Switching
Message Switching
Packet Switching
Virtual Circuit Switching
Datagram Switching

## Slide 3: Network Topology
1. Bus Topology
2. Mesh Topology
3. Ring Topology
4. Start Topology

## Slide 4: Bus Topology
Bus Topology
Single central cable (backbone) connects all devices.
Data travels in both directions along the cable.
Advantages:
  Easy to set up.
  Requires less cable than other topologies.
  Cost-effective for small networks.
Disadvantages:
  Limited cable length and number of nodes.
  If backbone fails, the entire network goes down.
  Difficult to troubleshoot.

## Slide 5: Mesh Topology
Mesh Topology
Every device connects directly to every other device.
Advantages:
  High fault tolerance and redundancy.
  Excellent reliability and data privacy.
Disadvantages:
  Expensive due to cabling and hardware.
  Complex setup and maintenance.

## Slide 6: Start Topology
Star Topology
All devices are connected to a central hub or switch.
Data passes through the hub to reach other devices.
Advantages:
  Easy to install and manage.
  Failure of one device doesn’t affect the rest.
Disadvantages:
  If the central hub fails, the whole network goes down.
  Requires more cable than bus or ring.

## Slide 7: Ring Topology
Ring Topology
Each device is connected to two others, forming a circular pathway.
Data travels in one direction (or both, in a dual ring).
Advantages:
  Predictable data flow reduces collisions.
  Performs better than bus under heavy load.
Disadvantages:
  A break in the ring can disrupt the entire network.
  Adding or removing nodes can be complex.

## Slide 8: Switching Mechanism for Data Transfer
Taxonomy of Switched Network

## Slide 9
Circuit Switching
Dedicated communication path between two stations
Must have switching capacity and channel capacity to establish connection
Must have intelligence to work out routing
Inefficient
  Channel capacity dedicated for the whole duration of connection
  If no data, capacity wasted
Set up (connection) takes time
Developed for voice traffic (phone)
Examples
  Telephone networks
  ISDN (Integrated Services Digital Networks)

## Slide 10
Circuit Switching
DATA
Set-up phase
Data Transfer phase
Teardown phase
A
B
Node 1
Node 2
propagation delay
between A
and Node 1
propagation delay
between B
and A
processing delay at Node 1

## Slide 11
Message Switching
No dedicated path needs to be established between end-nodes.
Source and destination node do not interact in real time. There is no need to determine the status of the destination node before sending the message.
Each message is an independent entity and carries address information of the destination. There is no upper limit on the size of the message.
The messages are stored at each node before being forwarded to the next node in the route.
Message switching accept all traffic but offers longer delivery time than circuit switching. Circuit switching blocks/rejects access traffic.
Header
Data

## Slide 12
Packet Switching
Messages are broken into small segments of bit-sequences and they are called packets. As packets are restricted to a specific size, they can be routed more rapidly.
Packets have the following structure:
    Header carries control information (e.g., destination id, source id, message id, packet id, control info)
Each packet is passed through the network from node to node along some path (Routing)
At each node the entire packet is received, stored briefly, and then forwarded to the next node (Store-and-Forward Networks)
Typically no storage is required at nodes/switches for packets.
Header
Data

## Slide 13
Packet Switching Advantages
Packetization allows short messages to get through a transmission link without waiting behind long messages.
Line efficiency
  Single node to node link can be shared by many packets over time
  Packets queued and transmitted as fast as possible
Packets are accepted even when network is busy
  Delivery may slow down
Priorities can be used

## Slide 14
Datagram packet switching
Modify as appropriate…..
Each packet is independently switched
  each packet header contains destination address
No resources are pre-allocated (reserved) in advance
Routes may change during session

## Slide 15
Delay in datagram network
There are three transmission times (3T), three propagation delays (slopes 3π of the lines), and two waiting times (w1 + w2). We ignore the processing time in each switch.
The total delay = 3 T + 3 π + w1 + w2

## Slide 16
Virtual-Circuit Packet Switching
Preplanned route established before any packets sent
Call request and call accept packets establish connection (handshake)
Communication with virtual circuits takes place in three phases
  VC establishment
  data transfer
  VC disconnect
Note: packet headers don’t need to contain the full destination address of the packet

## Slide 17
Delay in a virtual-circuit network
There are three transmission times (3T ), three propagation times (3π),
A setup delay, and a teardown delay. We ignore the processing time in each switch.
The total delay time is
Total delay = 3T + 3π + setup delay + teardown delay

## Slide 18
Datagram vs. Virtual-Circuits Packet Switching
Datagram | Virtual circuits
No call setup phase Better if few packets More flexible Routing can be used to avoid congested parts of the network | Network can provide sequencing and error control Packets are forwarded more quickly No routing decisions to make Less reliable Loss of a node looses all circuits through that node

## Slide 19
Books
1. Forouzan, B. A. "Data Communication and Networking. Tata McGraw." (2005).

## Slide 20
References
1. Prakash C. Gupta, “Data communications”, Prentice Hall India Pvt.
2. William Stallings, "Data and Computer Communications”, Pearson
3. Forouzan, B. A. "Data Communication and Networking. Tata McGraw." (2005).